## Slide 1
Monitoring of Solar system planets and detection of exoplanets by space telescopes Planetary Monitoring and Stellar Patrol
A. Tavrov, A. Kiselev, I. Vinogrdov, V. Ananjeva , V. Gnedykh, N. Sanko, L. Ksanfomaliti, O. Koravlev
Space Research Institute of RAS
Moroz V. I. 1931—2004

## Slide 2: Outline
Planetary monitoring – the pilot project of 0.6 m. telescope on RS ISS
Stellar Patrol – extended project of 1.5 m. telescope an orbital observatory
Missions’ aims:
  Monitoring of Solar System planets
  Engineering run to image exoplanets
Telescope instruments
Project phase …when to launch …etc.

## Slide 3
Mars
Water vapor & isotopic ratio of HDO/H2O
Methane (CH4)
Ozone (O3)
Dust storm & clouds
Planetary monitoring telescope: mission aims
The planetology studies the internal structure, the surface and the atmosphere of planets. Theoretical models and experimental methods combine the orbital telescope observations with planetary landing missions. The both results add and re-check each other. Mostly accessible for orbital observation are the Earth group planets, gas giants and their satellites.
Venus
Sulfur-contained components
UV absorber
Night glow
Atmosphere dynamics
Icy satellites of planets
Composition of comets
Giant planets
Lunar exosphere
Engineering run for exoplanets imaging
Meteor showers
Asteroid hazards
Space debris
Monitoring of orbital events…etc.

## Slide 4
We aim to equip the RS ISS with a telescope (of a Ø 600 mm primary mirror: angular resolution - 0.2 arc second), a two-axis guiding platform and science instruments: CCD photometer, stellar coronagraph, spectrometers and a spectro-polarimeter in UV, visible and NIR wavelength range.
Telescope Т600 projected view
Telescope placement on two -axis rotating platform
Planetary monitoring –telescope on the Russian Segment of ISS

## Slide 5
Platform pointing error ~ 10 arc. min
Pointing error compensation by a low mass secondary mirror tilt on hexapod driver
Science instruments
container
Planetary monitoring telescope construction details: mass 100 kg,
outer diameter 650 mm,
length 2200/1200 mm

## Slide 6
1. High resolution IR spectro-meter R>10000, λ=1..4 μm
2, 3. (FTS) Static Fourier Transform Spectrometer & Spectropolarimeter unit λ= 0,23..0,4 μm
Planetary monitoring telescope equipped by 5 instruments
4. Photometer with filters wheel (U, V, B, G, R, I):
imaging CCD 1530х1020 pixel,
guiding functions.
TIMM Phobos-Grunt
prototype
Co-operation with Ukraine

## Slide 7
5. Stellar achromatic coronagraph: λ=0.6..3 μm
Schematics
Планета
Звезда и планета
Темный выход
Светлый выход
CAD & lab. experiment
Low resolution NIR spectrometer

## Slide 8
Planetary monitoring telescope project phase

## Slide 9
Mars
Water vapor & isotopic ratio of HDO/H2O
Methane (CH4)
Ozone (O3)
Dust storm & clouds
Stellar Patrol – 1.5 m.
orbital observatory telescope: mission aims
Exoplanets imaging by nearest stars within a 5..10 pc. radius,
Low spectral resolution analysis of exoplanets (color analysis)
Exoplanet transit by the known RV-candidates
Solar system planetary monitoring
Astrophysical targets
Icy satellites of planets
Composition of comets
Giant planets
Lunar exosphere
Meteor showers
Asteroid hazards
Space debris
Monitoring of orbital events…etc.
Venus
Sulfur-contained components
UV absorber
Night glow
Atmosphere dynamics

## Slide 10
Stellar Patrol – a 1.5 m.
orbital observatory: telescope parameters
mass 500 kg
1.5 meter primary mirror diameter telescope
axial Ritchie Ch instruments planetary ~ 1 arc. min rétien optical scheme or other
wavelengths range: λ=0.25..3 µm
field of view:
      telescope ~ 2 arc. min
      instruments planetary ~ 1 arc. min
      instruments exoplanetary ~ 1 arc. sec
telescope length ~ 5 m
Orbit under study
lifetime 5…7 years
mass 500 kg
1.5 meter primary mirror diameter telescope
axial Ritchie Ch instruments planetary ~ 1 arc. min rétien optical scheme or other
wavelengths range: λ=0.25..3 µm
field of view:
      telescope ~ 2 arc. min
      instruments planetary ~ 1 arc. min
      instruments exoplanetary ~ 1 arc. sec
telescope length ~ 5 m
Orbit under study
lifetime 5…7 years

## Slide 11
Stellar Patrol
orbital observatory: platform parameters
NAVIGTOR platform Ok
http://www.oact.inaf.it/wso/
wic-jun06/28_06/NV-platform-rus.ppt#3
sci. instrumental mass up to 2500 kg
pointing error ± 2 arc. min (row) /
  ± 2.5 arc. sec under stabilization
electric power 1500 kWt

## Slide 12
Construction 2016-2024
Stellar Patrol – orbital observatory telescope: project phase
Launch 2025

## Slide 13
Orbital telescope with stellar coronagraph
Exoplanets imaging by nearest stars within a 5..10 pc. radius,
Low spectral resolution analysis of exoplanets (color analysis)
Exoplanet transit by the known RV-candidates
Solar system planetary monitoring
Astrophysical targets
Habitable zone
The companion appears clearly
in the coronagraphic image

## Slide 14
Conclusions
Planetary monitoring – the pilot project of 0.6 m. telescope on RS ISS
Stellar Patrol – extended project of 1.5 m. telescope an orbital observatory
We are at the very begin phase
Both projects are open for discussion to consider your science program

## Slide 15
Thank you!